## Slide 1: Software Defined Networks and the Maturing of the Internet
Nick McKeown
Stanford University

## Slide 2: Software Defined Networks and the Maturing of the Internet
Nick McKeown
Stanford University

## Slide 3: Software Defined Network (SDN)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Control
Control
Control
Control
Control
Global Network Map
Control Plane
Control
Program
Control
Program
Control
Program

## Slide 4: Network Function Virtualization (NFV)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Middlebox
Middlebox
Middlebox
Middlebox
Public Internet

## Slide 5: Network Function Virtualization (NFV)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Middlebox
Public Internet
VM
VM
VM
VM
VM
VM
Packet
Forwarding
Packet
Forwarding

## Slide 6: “Software will eat the world”
Marc Andreessen

## Slide 7
David D. Clark
Chief Protocol Architect, Internet
1981 - 1989

## Slide 8: Architectural Principles
Dumb and simple
i
Network: Streamlined, fast, low-cost, easy to maintain, infrequent upgrades.
1

## Slide 9: Architectural Principles
Decentralized control
i
Rapid organic growth
1969
2
Notes: : Four nodes
UCLA, SRI, UCSB, Utah.

## Slide 10
The Opte Project
Notes: Clearly this is way beyond something a human can do in their head. (Well, me at least – maybe you can).
So we need automated algorithms to calaculate the route and put the necessary fwding entries into the forwarding tables in the routers.
To calculate the routes, the routers will exchange information with each other about the current topology.
This is the job of what we call the Routing Algorithm or the Routing Protocol.
In some cases, the algorithm to calculate the route is wrapped in with the exchange of the state. In other cases, they are separate.
WE will look at both.

## Slide 11: The Internet was deliberately designed …
To be simple and streamlined.
To have decentralized control: Lots of individually controlled pieces.
Which led to …
Explosive organic growth of the Internet.
A great business for companies selling routers.
simple and streamlined
A great business
Notes: About $100B per year. 70% gross profit margin. Which means for every $100 of goods sold, they cost $30 to build. Not bad.
There is a business paradox here. Or rather, the situation is not stable: Simple and Streamlined is at odds with “A great business” <click>
There are two ways to break the instability: Either the Internet becomes a simple and streamlined commodity and is not particularly profitable. This would have been the social good.
Or, we break the simple and streamlined to justify keeping the profit margins high, and keeping others out of the business.
Which would you do if you had a very successful, great business?

## Slide 12: Strategy 1: Vertical integration
Proprietary
Operating System
Proprietary
Hardware
Proprietary
Features
“CLI”
Network Management
Notes: Vertical Integration: Make sure all the intelligence stays on the box, so you can command a high premium.
Typically a 75% margin business, which means for $1M router, $750k is profit.
One danger: Customers who manage very large networks will start moving the intelligence up into what is usually called “network management”. They will want to do this because:
1. Expertize: Customers operate big networks, so they understand the problems best
2. Differentiate: It allows them to differentiate their network from their competitors.
3. OPEX: They have uniform control over many boxes, from different vendors
4. CAPEX: It reduces cost.
So if you sell routers, you want to make sure that doesn’t happen!
This is true for routers, firewalls and most kinds of middlebox.
For years, the router vendors have made sure the control port is really simple and dumb.
Also called the CLI or command line interface.
Even today, most networks are managed by administrators logging into each router, or at best using screen-scraping to parse the CLI.

## Slide 13: Strategy 2: High barrier to entry
Notes: Once you’ve picked a strategy of vertical integration, the next step is to make no-one else can compete with your vertically integrated box.
The best way is to make sure the development cost is too high. You do this by increasing the number of features you have to support.

## Slide 14: Number of published Internet Standards
Chart: 
Notes: First one published April 7, 1969
Many of these are written and published by the router companies themselves…..

## Slide 15
50+ million lines of code
Tens of billions of gates
Routers are fragile, insecure, bloated and power hungry.
Like computer mainframes in the 1980s.
“Great business” triumphed over “simple and streamlined”.
Proprietary
Operating System
Proprietary
Hardware
Proprietary
Features
Notes: The consequence: Routers bloated, expensive, fragile and insecure….
We can argue about the details; but it couldn’t be any other way, because the market is making it so.
So what to do?

## Slide 16: Cisco Stock Price
1991
1999
200x
Google Finance

## Slide 17: How Data Center Owners Responded

## Slide 18: 2000: Rack-mounted Servers
Dell Servers
HP Servers

## Slide 19: 2005: The baremetal server
Sheet metal
DRAM
CPU
Power supply + fans
Linux
Notes: 2.5Billion transistors --- 100,000 times bigger. 4GHz --- 10,000 times faster
Taiwan

## Slide 20: Baremetal + Linux + Apps
Sheet metal
DRAM
CPU
Power supply + fans
Linux
Programmable
Hardware
Open-source
Software
App
App
App
Proprietary
Software
Notes: 2.5Billion transistors --- 100,000 times bigger. 4GHz --- 10,000 times faster
Taiwan

## Slide 22: Dell Stock Price
Google Finance
$42
$14
2005
2013

## Slide 23: 2012: The baremetal switch
Sheet metal
DRAM
CPU
Power supply + fans
Linux
xChip
Notes: 2.5Billion transistors --- 100,000 times bigger. 4GHz --- 10,000 times faster
Taiwan

## Slide 24: Baremetal + Linux + App
Sheet metal
DRAM
CPU
Power supply + fans
Linux
xChip
Open-source
P4
App
App
App
Proprietary
Software
Programmable
Hardware
Open-source
Software
Notes: 2.5Billion transistors --- 100,000 times bigger. 4GHz --- 10,000 times faster
Taiwan

## Slide 25: It’s happening fast!

## Slide 26: OCP: Wedge switch (open-source design)
BCM xChip: 1.2Tb/s

## Slide 27
DRAM
CPU
Power supply + fans
Linux
xChip
Optional Remote API
Open-source
ONL
API/Driver
Open-source
OF-DPA
Open-source
P4
Forwarding Agent
Open-source
FBOSS, OVS, Indigo, SwLight.
Network Controller
Open-source
ONOS, ODL
NOX, POX, Ryu
Floodlight, Beacon
Open-source
ONIE
Boot Loader
App
App
App
Proprietary
Software
Notes: 2.5Billion transistors --- 100,000 times bigger. 4GHz --- 10,000 times faster
Taiwan

## Slide 28: Big data centers use baremetal switches
Cost
400,000 servers
20,000 switches
$5k vendor switch = $100M
$1k bare-metal switch = $20M
Savings in 10 data centers = $800M
Control
Tailor network to applications
Proprietary behavior
Quickly debug

## Slide 29: Two great explanations
Google
Microsoft

## Slide 30: Now ISPs and Telcos are Starting to Respond

## Slide 31: The Problem
Global IP traffic growing 40-50% per year
End-customer monthly bill remains unchanged
Therefore, cost of ownership needs to reduce 40-50% per Gb/s per year
But in practice, reduces by <20% per year
$30/month
time
Growth in traffic
Revenue
Total cost

## Slide 32: Baremetal + Linux + Apps
Reduce capital cost
  Move to baremetal switches + Linux
Reduce operational cost
  Streamline protocols, features and software
Increase price
  Differentiate with new proprietary software services

## Slide 33: Baremetal + Linux + Application
Search
Facebook
YouTube
Netflix
Amazon
Network:
Baremetal
xChip/x86 + Linux
(500 thousand/yr)
Compute:
Baremetal
x86 + Linux
(10 million/yr)
Public Internet
Telcos/Cable
Open
Connect
B4
Swan
Google Fiber
Google WiFi
ARM + Linux
Baremetal
xChip/x86 + Linux/BSD
Notes: It’s the way the whole industry it headed….

## Slide 34: On SDN
“Because there is no army that can hold back an economic principle whose time has come.”
John Donovan, AT&T (2014)
Cisco 2014
  #1 Competitor: A software company (VMware)
  #1 Fear: Baremetal switches
Notes: Creation of ONF: Move to baremetal switches + open-source software, controlled by ISPs and data center owners.
Domain 2.0: Moving $21B of capex per year towards SDN and NFV. More than all the big 4 DC combined

## Slide 35
Server
Switch
Radio
VM
Linux
Linux
Linux
Linux
Programmable
Hardware
Open Source
Software
PIC
Linux
Remote Control Plane
Routing, Traffic Engineering,
Mobility, VPN
Proprietary
Software
DPI, Load Balance, SPAM
New Services
Overall System Management

## Slide 36
Notes: 20minutes

## Slide 37: SDN and NFV inevitable because…
Rise of Linux.
Rise of baremetal servers and switches.
NFV: Rise of virtualization.
SDN: Rise of merchant switching silicon.

## Slide 38: How switching chips are evolving

## Slide 39: Today: Fixed function switches
Combine
In
Queues
Data
Out
ACL Stage
L3 Stage
L2 Stage
Action: set L2D
Stage 1
L2 Table
L2: 128k x 48
Exact match
Action: set L2D, dec TTL
Stage 2
L3 Table
L3: 16k x 32
Longest prefix
match
Parser
…
Stage 3
ACL: 4k
Ternary match
Action: permit/deny
ACL Table
Action
Stage 16
Match
Etc.
Data
Header
Header
Data

## Slide 40: Packet Forwarding Speeds
Chart: 
| 1990.0 | 1995.0 | 2000.0 | 2005.0 | 2010.0 | 2015.0 | 2020.0
Switch Chip | 0.4 | 8 | 10 | 100 | 640 | 3200 | 14000
CPU | 0.1 | 1 | 2 | 5 | 20 | 80 | 200
Gb/s
(per chip)
3.2Tb/s

## Slide 41: Packet Forwarding Speeds
Chart: 
| 1990.0 | 1995.0 | 2000.0 | 2005.0 | 2010.0 | 2015.0 | 2020.0
Switch Chip | 0.4 | 8 | 10 | 100 | 640 | 3200 | 14000
CPU | 0.1 | 1 | 2 | 5 | 20 | 80 | 200
50x
Gb/s
(per chip)
3.2Tb/s

## Slide 42: Why the difference
Packet processing is inherently parallel
  Packets from different interfaces can be processed at same time
  Deep pipelines
Switching chips are dominated by I/O
  3.2Tb/s = 128 x 25Gb/s serial I/O

## Slide 43: Switch chips
Memory
(match tables and packet buffers)
Lots of Serial I/O
(10Gb/s or 25Gb/s)
Wires
(pipeline busses)
Logic
(everything else)
Notes: About 50% of area on serial I/O, 25% on memory, everything else is wire and logic.
About 4M transistors per sq mm today – logic is “free”.

## Slide 44: Problems: Fixed function switching chips
Slow innovation Several years to add a new feature or protocol
Inefficient Match tables hard-wired to specific purpose
Complicated Switch implements superset of all features
Leads to bottom-up design Frustrating for programmers

## Slide 45
“This is how I process packets”
(Datasheet)
Fixed-function ASIC
Run-time API
Switch OS

## Slide 46: Software Defined Everything
App
CPU
Computers
Compiler
GPU
Graphics
App
Compiler
DSP
Cellular Base Stations
App
Compiler
Networks
?
App
Compiler

## Slide 47: The RMT Architecture
Ingress Match+Action
Egress Match+Action
Queues
Protocol independence
Initially, switch chip is unprogrammed.
It does not know any protocols.
It does not know how to forward packets.
Parser
Notes: Chip design dominated by:
I/O
Memory
Wire
(Logic is almost free)

## Slide 48
Parser
Ingress Match+Action
Egress Match+Action
Queues
Protocol
Authoring
1
Compiler
Compile
2
Configure
3
TCP
New
IPv4
IPv6
VLAN
Eth
dc.p4
(P4 code)

## Slide 49
Parser
Ingress Match+Action
Egress Match+Action
Queues
TCP
New
IPv4
IPv6
VLAN
Eth
Protocol
Authoring
1
Compiler
Compile
2
Configure
3
dc.p4
(P4 code)
Run!
4
Add/delete table rules
Switch OS
Run-time API

## Slide 50
Programmable switch
Run-time API
“This is how the switch must process packets”
(Program)
Switch OS
The P4 Programming Language
(www.p4.org)

## Slide 51: Observations about switch chips
Chip design dominated by: (1) I/O, (2) Memory, (3) Wire.
There is no power, performance or area penalty for programmability
The fastest switching chips will be programmable
In private networks, “standard protocols” will be replaced by “programs”

## Slide 52: While computers became easier to use and more reliable…
1960s
1960s
1980s
1980s
2000s
Now
2000s
Now

## Slide 53: Networks became harder to manage and less reliable…
Now
Now

## Slide 54: Making Networks Work (Today)
traceroute, ping, tcpdump, SNMP, Netflow
…. er, that’s about it.

## Slide 55: Networks are kept working by “Masters of Complexity”

## Slide 56: Making Chips Work
Specification
Functional Description (RTL)
Functional Verification
Logical Synthesis
Static Timing
Place & Route
Design Rule Checking (DRC)
Layout vs Schematic (LVS)
Layout Parasitic Extraction (LPE)
Manufacture
& Validate
Testbench & Vectors
Automatic Test Vector Generation (ATVG)
Dynamic troubleshooting to Identify root cause
Formal specification languages
Static checking of lowest level design
Multiple layers of abstraction
Strong foundation (Boolean algebra)

## Slide 57: Making Chips Networks Work
Policy
Control
Program
Control
Plane
Dynamic troubleshooting to Identify root cause
Formal specification languages
Static checking of lowest level design
NETWORK
Automatic Test Pkt Generation (ATPG)
Frenetic, NetCore, Pyretic, Procera, … [2012]
Anteater, HSA [2011]
Dynamic checking of lowest level design
Veriflow, NetPlumber [2012]
ATPG [2012], NetSONAR [2013]
WWW, ndb [2012]
Consistent
Updates
(several) [2012]
Packet
Forwarding

## Slide 58: Even simple questions are hard
Can host A talk to host B?
What are all the packets from A that can reach B?
Are there any loops in the network?
Is Group X provably isolated from Group Y?
What happens if I remove a line in a config file?

## Slide 59: More interesting questions
When I add a new forwarding rule, how can I dynamically check in real-time if it will violate my network policy?
How do I track down the source code that was the root cause of a data plane error?
If switch hardware is malfunctioning, how will I know? How will I identify the switch/rule?

## Slide 60: Neither observe nor control
Complex interaction
  Between multiple protocols on a switch/router.
  Between state on different switches/routers.
Multiple uncoordinated writers of state.
Network owner can’t…
  Observe all state.
  Control all state.

## Slide 61: Header Space Analysis: Modeling Forwarding Behavior

## Slide 62: Header Space Analysis [NSDI ‘12]
A
B
L
Header
Data
01110011…1
Header
Data
111..100000

## Slide 63: Header Space Analysis
1
2
Match + Action

## Slide 64: The set of packets from A that can reach B
A
B

## Slide 65: All packets from A that can reach B
A
B

## Slide 66: Implications
Reachability and loops
Prove two groups are isolated
Regardless of protocol or layer
Analogy to Boolean algebra
Follow-on
  NetPlumber: Dynamic checking Google’s OpenFlow WAN 10,000 times per second
  ATPG: Test every forwarding rule 10-times per second

## Slide 67: When we look back in 20 years…
“Software will eat the world”
  SDN and NFV are a natural consequence of a bigger trend.
Network infrastructure will be:
  Baremetal + open-source infrastructure + proprietary apps
Network box vendors will be irrelevant
Network operators will have developed and will own proprietary software
Standards will have diminished value
Networks will be more reliable

## Slide 68: <The End>