## Slide 1: How SDNs will tame networks
Nick McKeown
Stanford University

## Slide 2: As I was saying…
How big to make a backbone router buffer?
C
B

## Slide 3: Buffer Size
Throughput
25,000
100%
2,500,000
10Gb/s WAN
Number of packets
On-chip buffers
Smaller design
Lower power
t
Window Size
Buffer

## Slide 4: Buffer Size
Throughput
log(W)
25,000
~50
~ 90%
100%
2,500,000
10Gb/s WAN
Number of packets
20 pkts
Integrated all-optical
buffer [UCSB 2008]
On-chip buffers
Smaller design
Lower power

## Slide 5: Software Defined Networks
Martin Casado
Scott Shenker
Teemu Koponen
Guru Parulkar
+ many (brave) students

## Slide 6
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface

## Slide 7
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface

## Slide 8: Where SDN will be deployed
Multi-tenant “virtualized” data centers
  Public and private clouds
WANs
  Google WAN
  Eventually, public WANs
Enterprise networks
  Greater control, fewer middleboxes

## Slide 9: Where SDN will be deployed (2)
4. Home networks
  Outsourced management
5. Cellular Networks
  Separation of service from physical infrastructure
6. Research and Education Networks
  National backbones
  College campus networks

## Slide 10: Getting Started
OpenFlow Tutorial
  search: “OpenFlow Tutorial”
Mininet
  Network emulator
  Designed for emulating SDN networks
  Easy to use
  High performance (100 nodes on a laptop)
  search: “Mininet”

## Slide 11: Tool & Deployment Support
Open Networking Lab (ON.Lab)
  Independent non-profit lab
  Open source tools
  Help with deployments
  Based in Palo Alto
  Hiring…

## Slide 12: OpenFlow Switches?
Software switch
  Open vSwitch (openvswitch.org)
  Now part of Linux distribution
Hardware switches
  Announcements from several vendors
  HP, Brocade, NEC, …
  (You could ask Google for one of theirs )
Switch ASICs
  Current ASICs work, but not optimized for OpenFlow
  Expect some OpenFlow-optimized ASICs in 1-2 years

## Slide 13: An example: What’s possible in silicon
Stanford/TI Labs collaboration
64 x 10Gb/s
Multiple table support (>12 flexible stages)
64k TCAM entries (wide) for wildcards
128k hash table entries (wide) for exact matches
>1k queues per port
All OpenFlow counters
On-chip ARM CPU
Generic ALU-based action engine
With permission from Texas Instruments

## Slide 14
If you are in any doubt about whether OpenFlow/SDN will be deployed in the WAN:
Urs Hoelzle (Google) at Open Networking Summit 2012

## Slide 15: Making Networks Work
An intellectual framework for verifying, troubleshooting and debugging SDNs
New Research Area

## Slide 16
With SDN we can:
  Formally verify that our networks are behaving correctly.
  Identify bugs, then systematically track down their root cause.

## Slide 17
Ensuring correctness [Frenetic][HFT][Netcore] Nate Foster, Andrew Ferguson, Mike Freedman, Jen Rexford, Rob Harrison, Dave Walker, ++
Software Fault Localization [W3] Scott Shenker, Colin Scott, Kyriakos Zarifis, Andreas Wundsam.
Checking behavior [NICE] Marco Canini, Daniele Venzano, Peter Peresini, Dejan Kostic, Jen Rexford.
Checking Invariants [VeriFlow] Ahmed Khurshid, Wenxuan Zhou, Matthew Caesar, P. Brighten Godfrey
Consistent updates Mark Reitblatt, Rick McGeer, ++
Troubleshooting [OFRewind] Andreas Wundsam, Dan Levin, Srini Seetharaman, Anja Feldman
…

## Slide 18
Scott Shenker at 1st ONS in 2011
“The Future of Networking and the Past of Protocols”

## Slide 19: Software Defined Network (SDN)
Global Network View
Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Network OS
Abstract Network View
Control
Programs
Control
Programs
Control
Programs

## Slide 20: Software Defined Network (SDN)
Global Network View
Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
firewall.c
…
if( pkt->tcp->dport == 22)
dropPacket(pkt);
…
Packet
Forwarding
Network OS
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…

## Slide 21: How do other industries do it?

## Slide 22: Making ASICs Work
$10B tool business supports a $250B chip industry
Specification
Functional Description (RTL)
Testbench & Vectors
Functional Verification
Logical Synthesis
Static Timing
Place & Route
Design Rule Checking (DRC)
Layout vs Schematic (LVS)
Layout Parasitic Extraction (LPE)
Manufacture
& Validate
100s of Books
>10,000 Papers
10s of Classes

## Slide 23: Making Software Work
Static Code Analysis
Invariant
Checker
Interactive Debugger
Model Checking
Run-time Checker
Specification
Testbench
Functional Description (Code)
$10B tool business supports a $300B S/W industry
100s of Books
>100,000 Papers
10s of Classes

## Slide 24: Making Networks Work (Today)
traceroute, ping, tcpdump, SNMP, Netflow
…. er, that’s about it.

## Slide 25: Why debugging networks is hard
Complex interaction
  Between multiple protocols on a switch/router.
  Between state on different switches/routers.
Multiple uncoordinated writers of state.
Operators can’t…
  Observe all state.
  Control all state.

## Slide 26: Networks are kept working by “Masters of Complexity”
A handful of books
Almost no papers
No classes

## Slide 27: Philosophy of Making Networks Work
YoYo
“You’re On Your Own”
Yo-Yo Ma
“You’re On Your Own, Mate”

## Slide 28
With SDN we can:
  Formally verify that our networks are behaving correctly.
  Identify bugs, then systematically track down their root cause.

## Slide 29: Software Defined Network (SDN)
Global Network View
Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
firewall.c
…
if( pkt->tcp->dport == 22)
dropPacket(pkt);
…
Packet
Forwarding
Network OS
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
1
2
3
4

## Slide 30: Three of our projects
Static Checking [HSA] “Independently checking correctness”
Automatic Testing [ATPG] “Is the datapath behaving correctly?”
Interactive Debugging [ndb] “Finding bugs, and their root cause, in an operational network”

## Slide 31: 1. Static checking Independently checking correctness
Peyman
Kazemian
Hongyi
‘James’
Zeng
George
Varghese
(UCSD)

## Slide 32: Motivations
In today’s networks, simple questions are hard to answer:
  Can host A talk to host B?
  What are all the packet headers from A that can reach B?
  Are there any loops in the network?
  Is Group X provably isolated from Group Y?
  What happens if I remove a line in the config file?

## Slide 33: Software Defined Network (SDN)
Global Network View
Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
Packet
Forwarding
Network OS
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
Static Checker
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
“A can talk to B”
“Guests can’t reach PatientRecords”
Policy

## Slide 34: How it works Header Space Analysis

## Slide 35: Header Space Analysis
1
2
3
4
1
2
3
4
Port ID
A
B
A
B

## Slide 36: Header Space Analysis
1
2
3
4
1
2
3
4
Port ID
A
B

## Slide 37: Can A talk to B?
1
2
3
4
1
2
3
4
Port ID
A
B
Notes: ----- Meeting Notes (4/17/12 18:54) -----
Now let's ask the question of whether A can talk to B.

## Slide 38: All packets from A that can reach B
A
B

## Slide 39: Header Space Analysis [Kazemian NSDI ‘12]
Consequences
  Abstract forwarding model; protocol independent
  Finds all packets from A that can reach B
  Find loops, regardless of protocol or layer
  Can prove that two groups are isolated
Can verify if network adheres to policy

## Slide 40: HSA as a “foundation”
HAS enables many tools and methods
  Independent static checking
  In-line in-controller invariance checking
  Dynamic testing: Automatic test packet generation
  Dynamic testing: Automatic performance monitoring
Analogy to Boolean algebra for logic design

## Slide 41: Software
Hassel tool
  Reads Cisco IOS Configuration
  Checks reachability, loops and isolation
  C: 60ms for Stanford Backbone
  Python: 10 mins for Stanford Backbone
Code
  http://bitbucket.org/peymank/hassel-public

## Slide 42: Three of our projects
Static Checking [HSA] “Independently checking correctness”
Automatic Testing [ATPG] “Is the datapath behaving correctly?”
Interactive Debugging [ndb] “Finding bugs, and their root cause, in an operational network”

## Slide 43: 3. Interactive Debugging Finding bugs, and their root cause, in an operational network
Nikhil
Handigol
Brandon
Heller
Vimal
Jeyakumar
David
Mazières

## Slide 44: Backtrace: Software Programming
Function A():
u = B(v)
Function B():
w = C(x)
Function C():
y = error
Breakpoint
  “u == error”
Backtrace
  File “A”, line 10, Function A()
  File “B”, line 43, Function B()
  File “C”, line 21, Function C()

## Slide 45: Interactive Debugging with ndb
Problem
  When an operational network misbehaves, it is very hard to find the root cause.
Goal
  Allow users to define a Network Breakpoint.
  Capture and reconstruct the sequence of events leading to the breakpoint.

## Slide 46: Network Debugger
B
A
S
Breakpoint
Switch = S
IP src = A, IP dst = B
TCP Port = 22
Collector

## Slide 47: Network Debugger
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
Collector

## Slide 48
B
A
Network Virtualization
Control
Programs
Control
Programs
Control
Programs
Network OS
Flow Table State Recorder
<Flow Table State, Version>
<Packet ID, Version>
Collector

## Slide 49
Collector
Network Virtualization
Control
Programs
Control
Programs
Control
Programs
Network OS
<Match, Action>
<Match, Action>
<Port == 22, Drop>
<Match, Action>
<Match, Action>
<Match, Action>
Breakpoint
Switch = S
IP src = A, IP dst = B
TCP Port = 22
S

## Slide 50: Who benefits
Network developers
  Programmers debugging control programs
Network operators
  Find policy error
  Send error report to switch vendor
  Send error report to control program vendor

## Slide 51: Status
First working prototype of ndb
  Works without change to OpenFlow
Performance on Stanford backbone
  Collector could be just one server
Collector

## Slide 52
Collector
Network Virtualization
Control
Programs
Control
Programs
Control
Programs
Network OS
<Match, Action>
<Match, Action>
<Port == 22, Drop>
<Match, Action>
<Match, Action>
<Match, Action>
Breakpoint
Switch = S
IP src = A, IP dst = B
TCP Port = 22
S
firewall.c
…
if( pkt->tcp->dport == 22)
dropPacket(pkt);
…

## Slide 53: Software Defined Network (SDN)
Global Network View
Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
firewall.c
…
if( pkt->tcp->dport == 22)
dropPacket(pkt);
…
Packet
Forwarding
Network OS
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
1
2
3
4

## Slide 54
With SDN we will:
  Formally verify that our networks are behaving correctly.
  Identify bugs, then systematically track down their root cause.

## Slide 55: Software Defined Networks
Allows a stronger intellectual foundation to networking
Allows us to define the right abstractions
Will allow us to transfer technology much faster, in both directions
Is already closing the gap with industry

## Slide 56: The End