## Slide 1: Null Space Learning in MIMO Systems
Alexandros Manolakos
Wireless Systems Laboratory
Electrical Engineering, Stanford University
Joint work with: Yair Noam and Andrea Goldsmith

## Slide 2: Outline
Null Space Learning in Underlay MIMO Cognitive radios
  System Model
  Null Space Acquisition
  Null Space Tracking
Null Space Coherence Time
Null Space Learning in Cooperative Multipoint Networks
  System Model
  Null Space Acquisition (Homework)
  Null Space Tracking (Not in this tak)
  Underlay Cognitive Radios & CoMP

## Slide 3
interference
data
Underlay MIMO Cognitive Radios
If the SU knows
interference = 0
The Problem:
  How to obtain the null space without cooperation
Solution:
  The SU learns the null space blindly, without any cooperation, by listening the energy of the PU signal.
Compatible with current wireless systems.
Unlicensed user
Licensed user
  How to obtain the null space without cooperation

## Slide 4
Power Control
The SU-Tx choses intelligently the messages x(t)
The PU-Rx notifies PU-Tx to change its Transmit Power
The variation in the Transmit Power of the PU-Tx is sensed by the SU-Tx.
The SU-Tx chooses the next message x(t) based only on the increase or decrease of the sensed power from the PU-TX.
One Transmission Cycle (TC)
The whole process is only based on energy measurements
Underlay MIMO Cognitive Radios

## Slide 5
Power Control
Two Phases:
  Acquisition Phase:
    Iterative Algorithm
    The only information needed between iterations is where interference increased or decreased.
  Tracking Phase:
    The SU-Tx searches “around” the outdated version of the precoding matrix to find a new one.
    Allows simultaneous transmission of information to the SU-RX.
Learning = Acquisition & Tracking
Underlay MIMO Cognitive Radios

## Slide 6
Power Control
Learning = Acquisition & Tracking
Underlay MIMO Cognitive Radios
Main Assumption : SU-Tx has more antennas than the PU-Rx, i.e. .
G =

## Slide 7: Cyclic Jacobi Technique (CJT)
where
How can the SU-Tx eliminate the entry of without knowing ?
Technique for Eigenvalue Decomposition

## Slide 8
Let the line search accuracy.
The SU-Tx fixes the and searches for the optimal
  2. The SU-Tx uses the computed to find the optimal
Blind Jacobi Step
are given by:
…this optimization can be done with a sequence of two line searches.
Each line search is based only on “binary comparisons”.
How can the SU-Tx eliminate the entry of without knowing G?
Only Binary Comparisons

## Slide 9: Modifications for the Tracking Algorithm
3rd Modification
In the line search of the optimal fix to a “small” value such that the SU-Tx does not inflict excessive interference to PU-Rx.
1st Modification
When starting a new adaptation, do not start from the identity matrix, but from the outdated null space.
2nd Modification
It can be proved that using the 1st modification, the optimal has a small value. Thus, search in a smaller interval.
Main idea of the Tracking algorithm

## Slide 10: Overview of the BNST Algorithm
Yes
No
Search
Search

## Slide 11: Example
Secondary transmitter (SU-Tx) performs the Null Space Algorithm.
  Red Curve: The Interference at the primary receiver (PU-Rx) without Null Space Learning.
  Blue Curve: The Interference at the PU-Rx with Null Space Learning.
  All channels have Independent Rician Fading with maximum Doppler frequency of 3 Hz and K-factor of 6. Two antennas in ST and one antenna in PR.

## Slide 12: Example
Secondary transmitter (ST) performs the Null Space Algorithm.
  Blue Curve: Average Interference reduction at the PU-Rx as a function of the maximum Doppler frequency.
  All channels have Independent Rician Fading with K-factor of 3. Two antennas in ST and one antenna in PR.

## Slide 13: Acquisition vs Tracking
Tracking
Acquisition
-th percentile of decrease in interference
Tracking meets the Peak Interference constraints

## Slide 14: What if the PU-Rx changes Frequency?
If the new user that transmits in the frequency that the SU-Tx adapts, then the adaptation will not be severely affected.
The algorithm could still continue!

## Slide 15: Parallel Jacobi Technique
Assumption:
Interference channels are approximately the same for different uplink frequencies.
Jacobi Method can be implemented in parallel
The SU-Tx can send different learning signals to two or more frequencies.
Future Research direction

## Slide 16
Normalized Autocorrelation of a SISO channel :
Decrease in Interference (dB):
  Decrease in interference to the PU-Rx if the SU-Tx transmits at time using the null space calculated at time .
Null Space Coherence Time
Independent Rayleigh Fading using the Clarke’s model with
The null space changes faster than expected!
Null Space changes “faster” than the channel

## Slide 17: Cooperative Multipoint Networks
Cooperative Multipoint (CoMP) has recently emerged as an important feature of LTE-A.
  CSI is typically available only inside a BSG.
eNodeB
eNodeB
  Out-of-Group interference (OGI)
poor spectral efficiency
CoMP bottleneck: Out-of-Group Interference

## Slide 18: One Transmission Cycle (TC)
BSG1
BSG2
eNodeB
eNodeB
BSG2 transmits a learning signal for TFB seconds.
UE calculates q(t)
UE feeds back q(t) to BSG1
BSG1 sends q(t) to BSG2
UE
The eNodeB forwards the interference level

## Slide 19: Interference Feedback
Interference
Computation
, c: constant during the learning process
Affine function of the interference
Interference Level:
Examples
  Noise plus interference level
  SINR level
  Total received power

## Slide 20: Conclusions
Null Space learning in Underlay MIMO Cognitive Radios
  Cyclic Jacobi Technique and Modifications
  Only based on binary comparisons of Energy measurements
Null Space Coherence Time
  Smaller than the channel coherence time
Null Space learning in Cooperative Multipoint Networks
  The terminals only sense the interference levels
  Algorithmic complexity is on the side of the Base Stations.
Many new research directions

## Slide 21: Questions?
Thank You

## Slide 22: System Model
The received signal at UE1:
The antennas of BSG2 and UE1.
BSG1
BSG2
UE
eNodeB
eNodeB
Inter-group Communication
Out of Group Interference
Similar System Model as before

## Slide 23: Simulation Scenarios
Independent Rayleigh Fading with Doppler Frequency Fd Hz.
(NT,NR)={ (6,2) , (8,1) }.
TFB = 1 msec
Average OGI is 15 dB more than the noise floor.
Two performance measures
  Average decrease of the worst case interference compared to the case of no null space learning.
  Average decrease of the worst case interference before and after one algorithm sweep.
  where denotes the spectral norm.

## Slide 24: Simulation Results
Tracking is more robust in channel variations primarily because it is faster.
  NT=8, NR = 1, Tracking needs 64% less TCs than learning
  NT=6, NR = 2, Tracking needs 32% less TCs than learning
Tracking allows for Interference control during learning
  Worst case interference reduction
  Relative worst case Interference reduction

## Slide 25: Modified Cyclic Jacobi Technique (CJT)
where
How can the SU-Tx eliminate the entry of without knowing ?
…this optimization can be done with a sequence of two line searches.
Each line search is based only on “binary comparisons”.
Main idea of the Acquisition algorithm

## Slide 26: The Acquisition Algorithm
Define
Observe
Perform as many measurements as the elements in
  TC complexity
Each TC gives a linear constraint over
the elements of
Learning is sufficient to learn (but not necessary…)
Linear System of Equations