## Slide 1: EE360: Lecture 13 Outline Cognitive Radios and their Capacity
Announcements
  Progress reports due today, HW 2 posted
  March 5 lecture moved to March 7, 12-1:15pm, Packard 364
  Poster session scheduling (90 min): T 3/11: 12pm or 4pm; W 3/12: 4:30pm, F 3/14 12pm or 5pm.
Introduction to cognitive radios
Underlay cognitive radios
  Spread spectrum
  MIMO
Interweave cognitive radios
Overlay cognitive radios
Next lecture: practical cognitive radio techniques

## Slide 2: CR Motivation Scarce Wireless Spectrum
and Expensive
$$$

## Slide 3: Cognition Radio Introduction
Cognitive radios can support new wireless users in existing crowded spectrum
  Without degrading performance of existing users
Utilize advanced communication and signal processing techniques
  Coupled with novel spectrum allocation policies
Technology could
  Revolutionize the way spectrum is allocated worldwide
  Provide sufficient bandwidth to support higher quality and higher data rate products and services

## Slide 4: What is a Cognitive Radio?
Cognitive radios (CRs) intelligently exploit
available side information about the
Channel conditions
Activity
Codebooks
Messages
of other nodes with which they share the spectrum

## Slide 5: Cognitive Radio Paradigms
Underlay
  Cognitive radios constrained to cause minimal interference to noncognitive radios
Interweave
  Cognitive radios find and exploit spectral holes to avoid interfering with noncognitive radios
Overlay
  Cognitive radios overhear and enhance noncognitive radio transmissions
Knowledge
and
Complexity

## Slide 6: Underlay Systems
Cognitive radios determine the interference their transmission causes to noncognitive nodes
  Transmit if interference below a given threshold
The interference constraint may be met
  Via wideband signalling to maintain interference below the noise floor (spread spectrum or UWB)
  Via multiple antennas and beamforming
NCR
IP
NCR
CR
CR

## Slide 7: Underlay Challenges
Measurement challenges
  Measuring interference at primary receiver
  Measuring direction of primary node for beamsteering
Policy challenges
  Underlays typically coexist with licensed users
  Licensed users paid $$$ for their spectrum
    Licensed users don’t want underlays
    Insist on very stringent interference constraints
    Severely limits underlay capabilities and applications

## Slide 8: Ultrawideband Radio (UWB)
Uses 7.5 Ghz of “free spectrum” (underlay)
UWB is an impulse radio: sends pulses of tens of picoseconds(10-12) to nanoseconds (10-9)
  Duty cycle of only a fraction of a percent
A carrier is not necessarily needed
Uses a lot of bandwidth (GHz)
High data rates, up to 500 Mbps, very low power
Multipath highly resolvable: good and bad
Failed to achieve commercial success

## Slide 9: Null-Space Learning in MIMO CR Networks
Performance of CRs suffers from interference constraint
In MIMO systems, secondary users can utilize the null space of the primary user’s channel without interfering
Challenge is for CR to learn and then transmit within the null space of the H12 matrix
Can develop blind null-space learning algorithms based on simple energy measurements with fast convergence
  Guest lecture by Alexandros Manolakos on this Wednesday

## Slide 10: Capacity of Underlay Systems
The capacity region of an underlay system must capture rates for both primary and cognitive users
If there are no constraints on the cognitive users, this reduces to the capacity region of the network
Constraints on cognitive users translate to constraints on their transmission
  For example, reduced power, null-space transmission, etc.
Capacity region depends on how interference is treated at both the primary and cognitive receivers

## Slide 11: Example: 2 user network
Interference caused by CR to RX2: Y=hX
Assume an interference constraint at RX2 of h:
This translates to a power constraint at the CR transmitter
Capacities:
Ideas can be extended to larger networks/other constraints
RX1
RX2
X
Primary
CR
X
h2
Y=h2X
h1
h3
Ytot=h2X+h3X’+Z
X’

## Slide 12: Summary of Underlay MIMO Systems
Null-space learning in MIMO systems can be exploited for cognitive radios
Blind Jacobi techniques provide fast convergence with very limited information
These ideas may also be applied to white space radios

## Slide 13: Interweave Systems: Avoid interference
Measurements indicate that even crowded spectrum is not used across all time, space, and frequencies
  Original motivation for “cognitive” radios (Mitola’00)
These holes can be used for communication
  Interweave CRs periodically monitor spectrum for holes
  Hole location must be agreed upon between TX and RX
  Hole is then used for opportunistic communication with minimal interference to noncognitive users

## Slide 14: Interweave Challenges
Spectral hole locations change dynamically
  Need wideband agile receivers with fast sensing
    Compresses sensing can play a role here
  Spectrum must be sensed periodically
  TX and RX must coordinate to find common holes
  Hard to guarantee bandwidth
Detecting and avoiding active users is challenging
  Fading and shadowing cause false hole detection
  Random interference can lead to false active user detection
Policy challenges
  Licensed users hate interweave even more than underlay
  Interweave advocates must outmaneuver incumbents

## Slide 15: Capacity of Interweave Channels
Capacity of CR depends on what white spaces are available and how accurately they are detected
Can model availability of white spaces via an on-off channel
Ergodic and outage capacity depend on probability of Toff/Ton
Misdetection leads to 2-state channel (with/without interference). Use capacity analysis for 2-state channels

## Slide 16: White Space Detection
White space detection can be done by a single sensor or multiple sensors
With multiple sensors, detection can be distributed or done by a central fusion center
Known techniques for centralized or distributed detection can be applied

## Slide 17: Detection Errors
Missed detection of primary user activity causes interference to primary users.
False detection of primary user activity (false alarm) misses spectrum opportunities
There is typically a tradeoff between these two (conservative vs. aggressive)

## Slide 18: Overlay Systems
Cognitive user has knowledge of other user’s message and/or encoding strategy
  Used to help noncognitive transmission
  Used to presubtract noncognitive interference
RX1
RX2
NCR
CR

## Slide 19: Transmission Strategy “Pieces”
Rate splitting
Precoding against interference at CR TX
Cooperation at CR TX
Cooperation atCR TX
Cooperation at CR TX
Precoding against interference at CR TX
To allow each receiver to decode part of the other node’s message  reduces interference
Removes the NCR
interference at the CR RX
To help in sending NCR’s message to its RX
Must optimally combine
these approaches
“Achievable Rates in Cognitive Radios” by Devroye, Mitran, Tarokh
Notes: It is CLEAR that it needs

## Slide 20: Results around 2007
b
a
1
1
weak
strong
interference
For Gaussian channel with P1=P2
Wu et.al.
Joviċić et.al.
New encoding scheme uses same techniques as previous work: rate splitting, G-P precoding against interference and cooperation
Differences:
More general scheme than the one that suffices in weak interference
Different binning than the one proposed by [Devroye et.al] and [Jiang et.al.]
M.,Y.,K

## Slide 21: Improved Scheme Transmission for Achievable Rates
Rate
split
NCR
CR
The NCR uses single-user encoder
The CR uses
- Rate-splitting to allow receiver 2 to decode part of cognitive user’s message and thus reduce interference at that receiver
- Precoding while treating the codebook for user 2 as interference to improve rate to its own receiver
- Cooperation to increase rate to receiver 2
RX1
RX2
NCR
CR

## Slide 22: Outer Bound
for input distributions that factor as
The set of rate triples (R0, R1,R2 ) satisfying
For R2=0, U2=Ø, and by redefining R0 as R2:
outer bound for the IC with full cooperation

## Slide 23: Outer Bound: Full Cooperation
The exact same form as the Nair-El Gamal outer bound on the broadcast channel capacity
The difference is in the factorization of the input distribution
reflecting the fact that only one-way cooperation is possible
The set of rate triples (R0, R1,R2 ) satisfying
for input distributions that factor as

## Slide 24: Summary of new technique
How far are the achievable rates from the outer bound?
Capacity for other regimes?
Achievable rates: combine
  rate splitting
  precoding against interference at encoder 1
  cooperation at encoder 1
Outer bound
Follows from standard approach: invoke Fano’s inequality
Reduces to outer bound for full cooperation for R2=0
Has to be evaluated for specific channels

## Slide 25: Performance Gains from Cognitive Encoding
  CR
  broadcast bound
  outer bound
  this scheme
  DMT schemes

## Slide 26: Cognitive MIMO Networks
Coexistence conditions:
  Noncognitive user unaware of secondary users
  Cognitive user doesn’t impact rate of noncognitive user
Encoding rule for the cognitive encoder:
  Generates codeword for primary user message
  Generates codeword for its message using dirty paper coding
  Two codewords superimposed to form final codeword
NCTX
CTX
NCRX
NCRX
NCRX
CRX
RX1
RX2
CR
NCR

## Slide 27: Achievable rates (2 users)
For MISO secondary users, beamforming is optimal
Maximum achievable rate obtained by solving
Closed-form relationship between primary/secondary user rates.

## Slide 28: MIMO cognitive users (2 Users)
Propose two (suboptimal) cognitive strategies
D-SVD
Precode based on SVD of cognitive user’s channel
P-SVD
Project cognitive user’s channel onto null space between CTX and NCRX, then perform SVD on projection

## Slide 29: Multi-user Cognitive MIMO Networks
Achievable rates with
two primary users
Cognitive MIMO network
with multiple primary users
Extend analysis to multiple primary users
Assume each transmitter broadcasts to multiple users
  Primary receivers have one antenna
  Secondary users are MISO.
Main Result:
  With appropriate power allocation among primary receivers, the secondary users achieve their maximum possible rate.

## Slide 30: Other Overlay Systems
Cognitive relays
Cognitive Relay 1
Cognitive Relay 2
Cognitive BSs

## Slide 31: Broadcast Channel with Cognitive Relays (BCCR)
Enhance capacity via cognitive relays
  Cognitive relays overhear the source messages
  Cognitive relays then cooperate with the transmitter in the transmission of the source messages
data
Source
Cognitive Relay 1
Cognitive Relay 2

## Slide 32: Channel Model
Sender (Base Station) wishes to send two independent messages to two receivers
Messages uniformly generated
Each cognitive relay knows only one of the messages to send

## Slide 33: Coding Scheme for the BCCR
Each message split into two parts: common and private
Cognitive relays cooperate with the base station to transmit the respective common messages
Each private message encoded with two layers
    Inner layer exposed to the respective relay
    Outer layer pre-codes for interference (GGP coding)

## Slide 34: Achievable Rate Region
Joint probability distribution
Achievable rate region: all rates (R12+R11,R21+R22) s.t.

## Slide 35: Generality of the Result
Without the cognitive relays
  BCCR reduces to a generic BC
  Correspondingly, rate region reduces to Marton’s region for the BC (best region to date for the BCs)
Without the base station
  BCCR reduces to an IC
  Correspondingly, rate region reduces to the Han-Kobayashi Region for the IC (best region for ICs)

## Slide 36: Improved Robustness
Without cognitive relays
  When base station is gone, the entire transmission is dead
With cognitive relays
  When base station is gone, cognitive relays can pick up the role of base station, and the ongoing transmission continues
  Cognitive relays and the receivers form an interference channel
data
Source

## Slide 37: A Numerical Example
Special Gaussian configuration with a single cognitive relay,
Rate region for this special case (obtained from region for BCCR)

## Slide 38: A Numerical Example
No existing rate region can be specialized to this region for the example except [Sridharan et al’08]
This rate region also demonstrates strict improvement over one of the best known region for the cognitive radio channel ([Jiang-Xin’08] and [Maric et al’08])
Channel parameters:
a = 0.5, b = 1.5;
P1 = 6, P2 = 6;

## Slide 39: Overlay Challenges
Complexity of transmission and detection
Obtaining information about channel, other user’s messages, etc.
Full-duplex vs. half duplex
Synchronization
And many more …

## Slide 40: Summary
Wireless spectrum is scarce: cognitive radios hold promise to alleviate spectrum shortage
Interference constraints have hindered the performance of underlay systems
  Exploiting the spatial dimension compelling
Interweave CRs find and exploit free spectrum:
  Primary users concerned about interference
Overlay techniques substantially increase capacity
  Can be applied to many types of systems
  uses all “tricks” from BC, MAC, interference channels
More details on channel capacity in tutorial paper (to be presented) and Chapter 2 of “Principles of Cognitive Radio”: to be posted
Very interesting to reduce these ideas to practice: much room for innovation

## Slide 41: Student Presentation
“Breaking Spectrum Gridlock With Cognitive Radios: An Information Theoretic Perspective”
By Andrea Goldsmith, Syed Ali Jafar, Ivana Maric and Sudhir Snirivasa
Appeared in Proceedings of the IEEE, May 2009
Presented by Naroa