## Slide 1: EE360: Lecture 15 Outline Sensor Networks and Energy Efficient Radios
Announcements
  2nd paper summary due March 5 (extended by 2 days)
  March 5 lecture moved to March 7, 12-1:15pm, Packard 364
  Poster session W 3/12: 4:30pm setup, 4:45 start, pizza@6.
  Next HW posted by Wed, due March 10
Overview of sensor network applications
Technology thrusts
Energy-Efficient Radios
Energy-Efficient Protocols
Cross-layer design of sensor network protocols

## Slide 2: Wireless Sensor Networks Data Collection and Distributed Control
Hard Energy Constraints
Hard Delay Constraints
Hard Rate Requirements

## Slide 3: Application Domains
Home networking: Smart appliances, home security, smart floors, smart buildings
Automotive: Diagnostics, occupant safety, collision avoidance
Industrial automation: Factory automation, hazardous material control
Traffic management: Flow monitoring, collision avoidance
Security: Building/office security, equipment tagging, homeland security
Environmental monitoring: Habitat monitoring, seismic activity, local/global environmental trends, agricultural

## Slide 4: Wireless Sensor Networks
Revolutionary technology.
Hard energy, rate, or delay constraints change fundamental design principles
Breakthroughs in devices, circuits, communications, networking, signal processing and crosslayer design needed.
Rich design space for many industrial and commercial applications.

## Slide 5: Technology Thrusts
Wireless Sensor Networks
Analog Circuits
Ultra low power
On-chip sensor
Efficient On/Off
MEMS
Miniaturized size
Packaging tech.
Low-cost imaging
Networking
Self-configuration
Scalable
Multi-network comm.
Distributed routing and scheduling
Wireless
Multi-hop routing
Energy-efficiency
Very low duty cycle
Efficient MAC
Cooperative Comm.
Data Processing
Distributed
Sensor array proc.
Collaborative detection/accuracy improvement
Data fusion
System-on-Chip
Integration of sensing, data processing, and communication in a single, portable, disposable device
Applications

## Slide 6: Crosslayer Protocol Design in Sensor Networks
Application
Network
Access
Link
Hardware
Protocols should be tailored to the application requirements and constraints of the sensor network
Notes: Interdisciplinary research, design, and development very challenging, but necessary to meet the requirements of future wireless applications

## Slide 7: Energy-Constrained Nodes
Each node can only send a finite number of bits.
  Energy minimized by sending each bit very slowly.
  Introduces a delay versus energy tradeoff for each bit.
Short-range networks must consider both transmit and processing energy.
  Sophisticated techniques not necessarily energy-efficient.
  Sleep modes save energy but complicate networking.
Changes everything about the network design:
  Bit allocation must be optimized across all protocols.
  Delay vs. throughput vs. node/network lifetime tradeoffs.
  Optimization of node cooperation.
Notes: All the sophisticated high-performance communication techniques developed since WW2 may need to be thrown out the window.
By cooperating, nodes can save energy

## Slide 8: Transmission Energy
Circuit energy can also be significant

## Slide 9: Modulation Optimization
Tx
Rx

## Slide 10: Key Assumptions
Narrow band, i.e. B<<fc
  Power consumption of synthesizer and mixer independent of bandwidth B.
Peak power constraint
L bits to transmit with deadline T and bit error probability Pb.
Square-law path loss for AWGN channel

## Slide 11: Multi-Mode Operation Transmit, Sleep, and Transient
Deadline T:
Total Energy:
where a is the amplifier efficiency and
Transmit
Circuit
Transient Energy

## Slide 12: Energy Consumption: Uncoded
Two Components
  Transmission Energy: Decreases with Ton & B.
  Circuit Energy: Increases with Ton
Minimizing Energy Consumption
  Finding the optimal pair ( )
  For MQAM, find optimal constellation size (b=log2M)

## Slide 13: Optimization Model
min
subject to
Where

## Slide 14: MQAM
MQAM (AWGN), for a given :
min
s.t.
Spectral efficiency (b/s/Hz):
min
s.t.

## Slide 15: Total Energy (MQAM)

## Slide 16: Total Energy (MFSK)
MQAM:
-45dBmJ at 1m
-33dBmJ at 30m

## Slide 17: Energy Consumption: Coded
Coding reduces required Eb/N0
Reduced data rate increases Ton for block/convolutional codes
Coding requires additional processing
Is coding energy-efficient
If so, how much total energy is saved.

## Slide 18: MQAM Optimization
Find BER expression for coded MQAM
  Assume trellis coding with 4.7 dB coding gain
  Yields required Eb/N0
  Depends on constellation size (bk)
Find transmit energy for sending L bits in Ton sec.
Find circuit energy consumption based on uncoded system and codec model
Optimize Ton and bk to minimize energy

## Slide 19: Coded MQAM
Reference system has bk=3 (coded) or 2 (uncoded)
90% savings
at 1 meter.

## Slide 20: MFSK Optimization
Find BER expression for uncoded MFSK
  Yields required Eb/N0 (uncoded)
  Depends on b, Ton a function of b.
Assume 2/3 CC with 32 states
  Coding gain of 4.2 dB
  Bandwidth expansion of 3/2 (increase Ton)
Find circuit energy consumption based on uncoded system and codec model
Optimize b to minimize total energy

## Slide 21: Benefits of Coding

## Slide 22: Cooperative MIMO
  Nodes close together can cooperatively transmit
    Form a multiple-antenna transmitter
  Nodes close together can cooperatively receive
    Form a multiple-antenna receiver
  MIMO systems have tremendous capacity and diversity advantages

## Slide 23: MIMO
Tx:
Rx:

## Slide 24: MIMO: optimized constellations (Energy for cooperation neglected)

## Slide 25: Cross-Layer Design with Cooperation
Multihop Routing among Clusters

## Slide 26: Double String Topology with Alamouti Cooperation
Alamouti 2x1 diversity coding scheme
  At layer j, node i acts as ith antenna
Synchronization required
Local information exchange not required

## Slide 27: Equivalent Network with Super Nodes
Each super node is a pair of cooperating nodes
We optimize:
  link layer design (constellation size bij)
  MAC (transmission time tij)
  Routing (which hops to use)

## Slide 28: Minimum-energy Routing (cooperative)

## Slide 29: Minimum-energy Routing (non-cooperative)

## Slide 30: MIMO v.s. SISO (Constellation Optimized)

## Slide 31: Delay/Energy Tradeoff
Packet Delay: transmission delay + deterministic queuing delay
Different ordering of tij’s results in different delay performance
Define the scheduling delay as total time needed for sink node to receive packets from all nodes
There is fundamental tradeoff between the scheduling delay and total energy consumption

## Slide 32: Minimum Delay Scheduling
The minimum value for scheduling delay is T (among all the energy-minimizing schedules): T=å tij
Sufficient condition for minimum delay: at each node the outgoing links are scheduled after the incoming links
An algorithm to achieve the sufficient condition exists for a loop-free network with a single hub node
An minimum-delay schedule for the example: {2!3, 1!3, 3!4, 4!5, 2!5, 3!5}
1
2
3
4
5
T
T
4!5
2!5
3!5
1!3
2!3
3!4

## Slide 33: Energy-Delay Optimization
Minimize weighted sum of scheduling delay and energy

## Slide 34: Transmission Energy vs. Delay

## Slide 35: Total Energy vs. Delay

## Slide 36: Transmission Energy vs. Delay (with rate adaptation)

## Slide 37: Total Energy vs. Delay (with rate adaptation)

## Slide 38: MAC Protocols
Each node has bits to transmit via MQAM
Want to minimize total energy required
TDMA considered, optimizing time slots assignment (or equivalently , where )

## Slide 39: Optimization Model
min
subject to
Where are constants defined by the
hardware and underlying channels

## Slide 40: Optimization Algorithm
An integer programming problem (hard)
Relax the problem to a convex one by letting be real-valued
  Achieves lower bound on the required energy
Round up to nearest integer value
  Achieves upper bound on required energy
Can bound energy error
  If error is not acceptable, use branch-and-bound algorithm to better approximate
Notes: Number of bits to transmit is an integer

## Slide 41: Branch and Bound Algorithm
Divide the original set into subsets, repeat the relaxation method to get the new upper bound and lower bound
If unlucky: defaults to the same as exhaustive search (the division ends up with a complete tree)
Can dramatically reduce computation cost
b=1,…,8
b=1,…,4
b=5,…,8
b=1, 2
b=3, 4
b=3
b=4

## Slide 42: Numerical Results
When all nodes are equally far away from the receiver, analytical solution exists:
General topology: must be solved numerically
  Dramatic energy saving possible
  Up to 70%, compared to uniform TDMA.

## Slide 43: Minimum-Energy Routing Optimization Model
The cost function f0(.) is energy consumption.
The design variables (x1,x2,…) are parameters that affect energy consumption, e.g. transmission time.
fi(x1,x2,…)0 and gj(x1,x2,…)=0 are system constraints, such as a delay or rate constraints.
If not convex, relaxation methods can be used.
Focus on TD systems
Min
s.t.

## Slide 44: Minimum Energy Routing
Transmission and Circuit Energy
4
3
2
1
0.3
(0,0)
(5,0)
(10,0)
(15,0)
Multihop routing may not be optimal when
circuit energy consumption is considered
Red: hub node
Blue: relay only
Green: source

## Slide 45: Relay Nodes with Data to Send
Transmission energy only
4
3
2
1
0.115
0.515
0.185
0.085
0.1
Red: hub node
Green: relay/source
(0,0)
(5,0)
(10,0)
(15,0)
• Optimal routing uses single and multiple hops
• Link adaptation yields additional 70% energy savings

## Slide 46: Summary
Protocol designs must take into account energy constraints
Efficient protocols tailored to the application
For large sensor networks, in-network processing and cooperation is essential
Cross-layer design critical

## Slide 47: Cognitive radios are also sensor networks

## Slide 48: Presentation
Multiantenna-assisted spectrum sensing for cognitive radio.
By Wang, Pu, et al.
Appeared in IEEE Trans. Vehicular Technology, in 2010
Presented by Christina