## Slide 1: Energy-Efficient Communications Protocol for wireless microsensor networks
W. Heinzelman, A. Chandrakasan, H. Balakrishnan, Published in 2000

## Slide 2: Overview
Problem Description
Energy Models
Conventional Methods
LEACH Algorithm
Conclusions

## Slide 3: Sensor Network Reachback Problem
Sensor nodes distributed randomly (~U)
Homogenous, finite energy nodes
Distant processing station (Direct communication expensive)
Sensor coordination
  Clustering
  Preprocessing
Goal: Maximize lifetime of the system
  Detailed Energy model

## Slide 4: Energy Model
First-Order Model:
  ETx(k, d) = k (Eelec + d2 εamp)
  ERx(k) = k Eelec
k Number of bits/packet
d Distance to destination
Eelec Circuit energy/bit
εamp Amplifier Energy
Parameter values chosen for Bluetooth specifications
  Eelec = 50 nJ/bit
  εamp = 100 pJ/bit/m2

## Slide 5: Conventional Approaches
Direct Transmission: Every node communicates directly with processing station
Minumum Transmit Energy (MTE): Multi-hop routing to minimize distances
Problem: Uneven energy burden
  Leads to spatial death and poor sampling
X-coordinate
Y-coordinate
Y-coordinate
X-coordinate
Time Step
Number of Nodes Alive

## Slide 6: Clustering
Hybrid of Direct and MTE strategies
  Cluster head collects data from cluster (MTE)
  Compresses data
  Cluster head sends data to processing center (Direct)
However…
  Static clustering inherits drawbacks:
  Cluster heads die quickly
  Lose entire clusters at a time
Low Energy Adaptive Clustering Hierarchy (LEACH)

## Slide 7: LEACH: Adaptive Clustering
Self Organizing Clusters
  Nodes decide to become ‘cluster heads’ at each time step
Adaptive Clustering
  Choice determined by time since last choice and remaining energy
P – Desired percentage of cluster heads
T(n) – Decision threshold
r – current round
G – Set of nodes which have not been cluster heads in the last 1/P rounds
Optimal P depends on topology
Normalized Energy Dissipation
Percent of nodes that are cluster heads

## Slide 8: LEACH: Algorithm
Advertise
  Compare random variable ~U[0,1] to T(n)
Set-up
  Use RSS to determine which cluster to join
Schedule
  Cluster head sends TDMA schedule
Data Transmission
  Nodes send raw data to cluster head
  Cluster head compresses data
  Compressed data sent to processing station

## Slide 9: LEACH: Improves Network Lifetime
P = 5%, k = 2000
Life energy: 0.5J,
Compression: 5nJ/bit/packet
Random node death
Improves lifetime
  8x Direct
  6x MTE
Time Step
Network diameter (m)
X-coordinate
Number of nodes alive
Total Energy Dissipated (J)
Y-coordinate

## Slide 10: LEACH: Issues
Poor performance in very dense networks
Not guaranteed to have valid schedules
  Overloading one cluster head
Old Multi-access techniques
  CSMA, TDMA

## Slide 11: Conclusions
Detailed model uncovers new challenges
Adaptive approach for energy balancing
Significant improvement in lifetime
Paved the way for many other projects